## Slide 1: DSP Tutorial
Version | Date | Author | Notes
1.0 | Jan, 2014 | Yiwei Ma | First version; Suitable for DSP 28335 and CCS 5.0
1.1 | July, 2018 | Yiwei Ma | Modified template, adjusted slide sequence, Added instructions to the sample code

## Slide 2: DSP
Getting Started
  Hardware introduction: DSP 28335 CPU and peripherals
  Software introduction: CCS 5
    Project Structure Example
    Build a New Project
    Basic Knowledge for Debugging
DSP Programming
  Program Sequence
  Configure the DSP – Registers and Memory
    PWM, Interrupts
    Memory and CMD File
    External Interface (with ADC, FPGA, etc)
    Start from Flash
  Tips Based on Experiences
    Useful Tools Provided by CCS
    Programming Tips
Debugging with Converter – A Flowchart

## Slide 3: DSP Hardware introduction
Digital Signal Processor
  Texas Instrument DSP TMS320F28335
  Not the most advanced one, but majority of people still use it.
Parameters |  | Specs
Processor | CPU clock | 150 MHz, (6.67 ns Cycle Time)
Memory | RAM | 68 kB
 | Flash | 512 kB
PWM | PWM Channels | 6 ePWM modules, 12 output channels
 | High Resolution PWM Channels | 6 HRPWM Outputs With 150 ps MEP Resolution

## Slide 4: DSP Hardware introduction
Parameters |  | Specs
A/D converter | Channels | 16
 | Resolution | 12 bit
 | Input voltage range | 0 ~ 3.0V
 | Conversion time | 80 ns
D/A converter | NO DAC on eZdsp F28335 | 
Communications | USB | NO
 | RS-232 Serial port | 2
 | CAN bus port | 2
 | GPIO pins | 88
 | JTAG | 1

## Slide 5: Programming tool — CCS
Code Composer Studio v5
  Based on Eclipse
Eclipse
  An integrated development environment (IDE). It contains a base workspace and an extensible plug-in system for customizing the environment.
  Very common IDE for JAVA

## Slide 6: Project Structure Example
Project name
Software generated files
Directory For the header files
Produced programs
For DSP
Target Configurations:
Tells the types of the DSP and emulator.
Common source files:
Provide basic functions;
Usually the same for every projects.
User defined files:
Determine the functions of the project;
Can be more than one file.

## Slide 7: New Project
Output type: Executable
Family: C2000
Variant: 2833x Delfino EZDSPF28335
Connection: Spectrum Digital DSK-EVM-eZdsp onboard USB Emulator
Empty Project

## Slide 8: Add Source Codes to The Project
All files under “Source Code” folder
Copy or Link? Personal preference
Copy:
  You have your own copy of the codes. No need to worry about making change to the original files.
  Delete from workspace will delete it on your hard drive. Please backup your codes.
Link:
  The linked file is changed once you modify it. Easy to share your modification between projects. May cause problem if others are not aware of the change.
  Delete from workspace will NOT affect the original file.

## Slide 9: Add Search Path for Header File
Filesystem -> Your header file directory
“Include” folder

## Slide 10: Compile and Run
Run continuously (or to the next breakpoint)
Debug
(Automatically compile, build and load programs into DSP)
Double click here to create a breakpoint
To check all breakpoints you set
Someone may need to add a “CCS Debug” perspective
Most don’t.

## Slide 11: Debug - Run the Program
Leave Debug
Restart Program
Step into
Step over
Step return

## Slide 12: Debug - Observing Variables
Yellow background indicates value
different from previous.
Expression Tab to check variables
Register Tab to check registers
You can also check value of an expression
(e.g. Vt_pu*100=0.35…)

## Slide 13: DSP Programming
Program Sequence
Configure the DSP – Registers and Memory
  PWM, Interrupts
  Memory and CMD File
  External Interface (with ADC, FPGA, etc)
  Start from Flash
Tips Based on Experiences
  Useful Tools Provided by CCS
  Programming Tips

## Slide 14: Program Sequence

## Slide 15: Configure the DSP – Registers
Example: Enable ePWM1 interrupts
EPwm1Regs.ETSEL.bit.INTEN = PWM1_INT_ENABLE; // Enable INT
EPwm1Regs.ETSEL.bit.INTEN = 1; // Enable INT
EPwm1Regs.ETSEL.all |= 0x0008; // Enable INT
Defined as 1 at top of the program
Others can be found in related header files
void InitEPwmTimer()

## Slide 16: ePWM – Configuration
http://www.ti.com/lit/ug/sprug04a/sprug04a.pdf
TBPRD: Period
CMPA: Switch A (Lower)
CMPB: Switch B (Higher)
TBCTR: Counter
TBCTL.bit.CTRMODE: Shape
Carrier Wave
Modulation Wave
TB: Carrier Wave
CC: Modulation Wave
AQ: Set / Toggle Output PWM
DB: Generate Dead Band
PC: Generate High Freq. Pulses
TZ: Respond When Fault
ET: Trigger ADC or Interrupts

## Slide 17: ePWM – Double pulse logic signal generator
If (Flag_DPT == 1) // Enable double pulse signal //
{
// Set double pulse parameter //
sw_per=5700; // Tn*150MHz (clock speed)
Tn=6000; // Sw_per*150MHz (clock speed)
Tn1=600; // Tn1*150MHz (clock speed)
// Generate the 1st pulse //
if (DPT_count == 1) // DPT_count is pulse # account, initial value is set to be 1
{
EPwm1Regs.TBPRD = sw_per; // set EPWM1 period
// set EPWM1A register for S_L //
EPwm1Regs.CMPA.half.CMPA = Tn; // set EPWM1A comparator
EPwm1Regs.AQCTLA.bit.CAU = AQ_CLEAR; // set EPWM1A actions when counter equals the CMPA, force
EPWM1A output low
EPwm1Regs.AQCTLA.bit.ZRO = AQ_SET; // Initialize EPWM1A output, action when counter equals to 0, force
EPWM1A output high
// set EPWM1B register for S_H (always low) //
EPwm1Regs.CMPB = 0; // set EPWM1B comparator//
EPwm1Regs.AQCTLB.bit.CBU = AQ_CLEAR; // set EPWM1B actions when counter equals the CMPA, force
EPWM1B output low
EPwm1Regs.AQCTLB.bit.ZRO = AQ_CLEAR; // Initialize EPWM1B output, action when counter equals to 0, force
EPWM1B output low
DPT_count=2; // prepared for the 2nd pulse//
}
Double pulse logic signal

## Slide 18: ePWM – Double pulse logic signal generator
else // Generate the 2nd pulse //
{
if (DPT_count == 2)
{
EPwm1Regs.TBPRD = sw_per; // set EPWM1 period
EPwm1Regs.CMPA.half.CMPA = Tn1; // re-set EPWM1A comparator
EPwm1Regs.CMPB = 0; // set EPWM1B comparator
DPT_count = 3; // Complete double pulse signal generator//
}
else // After the 2nd pulse, disable PWM output
{
EPwm1Regs.TBPRD = sw_per; // set EPWM1 period
EPwm1Regs.CMPA.half.CMPA = 0; // re-set EPWM1A comparator
EPwm1Regs.AQCTLA.bit.ZRO = AQ_CLEAR; // Initialize EPWM1A output, action when counter
equals to 0 force EPWM1A output low
EPwm1Regs.CMPB = 0; // set EPWM1B comparator
}
}

## Slide 19: Interrupt – Configuration
http://www.ti.com/lit/ug/spru430e/spru430e.pdf
http://www.ti.com/lit/ug/spru566j/spru566j.pdf
For a successful interrupt, the following condition must be satisfied
Event
Correct Interrupt Function Address
Interrupt Enabled
PIEIER Enabled
PIEACK cleared
CPU Allow Interrupt

## Slide 20: HTB Program Sequence

## Slide 21: External Interface (XINTF) – Configuration
DSP can be connected to ADC, DAC, FPGA, etc.
XD(15:0): Data bus
XA(15:0): Address bus
: Zone chip-select
: Active low read signal
: Active low read signal
Physical connection
If DSP interfaces with multi-external device, then the address from DSP should be decoded to the CS(Chip Selection) signals
XA

## Slide 22: External Interface (XINTF) – Read/Write Process
// Read process // Write process
V=*(0x00200000) *(0x00200000)=V
// * represents addressing
// 0x00200000 indicates is active, and XA(15:0)=0x0 meaning CDAD1 is active
The time for the lead/active/trail period can be set

## Slide 23: Memory and CMD File
Linker Command (CMD) file
  Helps Compiler to allocate the program into different part of the DSP memories.
MEMORY
{
PAGE 0 :
…
RAML1 : origin = 0x009000, length = 0x002000
…
}
SECTIONS
{
…
.text : > RAML1, PAGE = 0
…
}
(Define memory blocks)
(Tell which section goes to which block)

## Slide 24: Memory and CMD File
int x = 2;
int y = 7;
void main(void)
{
long z;
z = x + y;
}
Global vars (.ebss)
Init values (.cinit)
Local vars (.stack)
Code (.text)
http://www.ti.com/lit/ug/spru513g/spru513g.pdf
http://processors.wiki.ti.com/index.php/C28x_Compiler_-_Understanding_Linking
Section Name | Description
.text | Executable code and constants
.cinit | Initalized global and static variables
.econst | Constant data (e.g. const int k = 3;)
.switch | Tables for switch statements
.ebss | Global and static variables
.stack | Stack space
.esysmem | Memory for malloc type functions
.reset | Reset vector

## Slide 25: Start from FLASH
FLASH data will not be erased after the power loss: No need to load program every time.
Procedure:
  Change CMD file, change “Boot Load Option Switch” on the development board
  Add “DSP2833x_MemCopy.c” to your project
  Put your calculation functions to RAM, in order to increase time efficiency
    #pragma CODE_SECTION(Your_Func_Name, "ramfuncs");
  Add following codes during initialization
    MemCopy(&RamfuncsLoadStart, &RamfuncsLoadEnd, &RamfuncsRunStart);
    InitFlash();
Example project can be downloaded from TI website.
Note that you can only have two breakpoints when using flash
http://www.ti.com/lit/an/spra958l/spra958l.pdf

## Slide 26: What Could Go Wrong
If there are errors or warnings shown.
  Google it, or ask in forums
If there are no explicit errors, but running have problems, generally possible reasons are:
  Broken DSP / Bad configuration on CCS / Emulator
  Breakpoints do not work (Programs run well)
  Jumper on Development Board is not set correctly
  Related registers are configured wrong or didn’t manually clear after an event.

## Slide 27: Links on help documents and resources
Official user guide
  http://www.ti.com/product/tms320f28335
Workshop presentation slides
  http://processors.wiki.ti.com/index.php/C2000_Archived_Workshops
Discussion forum
  http://e2e.ti.com/support/microcontrollers/c2000/f/171.aspx
Example projects
  http://www.ti.com/tool/sprc530

## Slide 28: Discussion
How can you tell PWM1 interrupts triggers before PWM2 interrupts? Or vice versa?
How many methods can you think of to double the LED toggle time periods?

## Slide 29: Useful Functions
Plot Graph from Cached Data
Save Cached Data
Compare with Local History
Memory Browser
Search All Files in Workspace
Useful Shortcut Keys
Clock

## Slide 30: Plot Graph from Cached Data
0
Save and load configurations
Variable name or address

## Slide 31: Graph
Double click to enlarge
Reload
Clear
Modify configuration

## Slide 32: Save Cached Data

## Slide 33: Local History
Especially helpful when you don’t remember what’s modified, or someone changed the program without telling you.

## Slide 34: Compare Files
Different places thorough the codes

## Slide 35: Memory Browser

## Slide 36: Search All Files in Workspace
CCS 5.5 may not have search tab, all the same to use the search icon

## Slide 37: Useful Shortcut Keys
Ctrl + / // Comment
Ctrl + / again Remove //
Ctrl + Shift + / /* */ Comment
Ctrl + Shift + \ Remove /* */
Ctrl + B Compile and Build
F5, F6, F7 Step over, into, return

## Slide 38: Clock
ZIP() function takes 1410/150MHz = 9.4us to run

## Slide 39: Tips to Increase Calculation Efficiency
Use “ * ” instead of “ / ”, use less sqrt() etc.
Calculate only once for frequently used expression
Change library (Ask Bo or Brad)
Homework
  If you are working on a project with DSP programming, please check the running time of your code, and try to optimize it.
Avg = (A+B)/2; | Avg = (A+B)*0.5;
if (sqrt(Vd*Vd+Vq*Vq)<2) | if ((Vd*Vd+Vq*Vq)<4)
Vd = cos(theta)*Vas + ((-0.5)*cos(theta) + 0.866*sin(theta))*Vbs + ((-0.5)*cos(theta) - 0.866*sin(theta))*Vcs; Vq = sin(theta)*Vas + (sin(theta)*(-0.5)-cos(theta)*0.866)*Vbs + (sin(theta)*(-0.5)+cos(theta)*0.866)*Vcs; | c_theta = cos(theta); s_theta = sin(theta); Vd = c_theta*Vas + ((-0.5)*c_theta + 0.866*s_theta)*Vbs + ((-0.5)*c_theta - 0.866*s_theta)*Vcs; Vq = s_theta*Vas + (s_theta*(-0.5) - c_theta*0.866)*Vbs + (s_theta*(-0.5) + c_theta*0.866)*Vcs;

## Slide 40: Tips on Programming
Readability
  Comments
    Good example from Zheyu’s double pulse program
  Meaningful variable and function names
  Indentation

## Slide 41: Other tips
Avoid array subscript out of range
Data type of a number
Avoid division by zero

## Slide 42: Converting the Continuous Simulation to DSP
How do you write this in DSP?
Integration |  | Integral = Integral + X * T_s;
Differentiation |  | Diff = (X_pre – X) / T_s; X_pre = X;
Saturation | N/A | if (X > Satur) { X = Satur; }
Transfer Fn. |  | Use Matlab “c2d” to get z-function Use anti-z-transformation to get time domain difference equation
Delay |  | X_pre = X;
Integration |  | Integral = Integral + X * T_s;
Differentiation |  | Diff = (X_pre – X) / T_s; X_pre = X;
Saturation | N/A | if (X > Satur) { X = Satur; }
Transfer Fn. |  | Use Matlab “c2d” to get z-function Use anti-z-transformation to get time domain difference equation
Delay |  | X_pre = X;
T_s is the switching cycle / calculation cycle

## Slide 43: Debugging with Converter